## Slide 1
Vidyut Prajna
AI-Driven Spatio-Temporal Intelligence for EV Charging Optimization & Infrastructure Planning
Bengaluru digital twin • H3 spatial grid • graph-temporal demand forecast • constraint-aware scheduling • LLM planner assistant
Non-invasive sidecar
No SCADA write-back
Planner decision support
Prototype repo + Dash app + LLM UX layer

## Slide 2
1. Problem: coincident EV charging peaks
Bengaluru distribution grid
Vidyut Prajna prototype • read-only planner sidecar • synthetic demo data
EV charging can overlap with residential and commercial evening peak windows.
City-wide load can look stable while individual DTRs experience localized thermal stress.
Demand is non-uniform: HSR residential evening charging differs from Peenya/Yeshwanthpur fleet demand.
BESCOM planners need predictive hotspots and safe load-shifting recommendations.
Core risk
Unmanaged charging creates localized overload events at distribution transformer level.
Planning question
Where will demand peak, why is it risky, and which flexible loads can move?
Deployment constraint
The solution must remain a read-only intelligence layer with zero hardware control.

## Slide 3
2. Proposed solution: a read-only intelligence sidecar
No control commands
Vidyut Prajna prototype • read-only planner sidecar • synthetic demo data
Telemetry
OCPP sessions
Traffic
Weather
Grid load
H3 grid
Bengaluru cells
Neighbor graph
Cell metadata
Forecast
Graph-aware GRU
Short-term demand
Risk score
Optimize
Priority constraints
Deadlines
Valley filling
Explain
Dash UI
LLM chat
Planner recommendations
Isolation barrier: outputs are recommendations, heatmaps and schedules only.

## Slide 4
3. Data simulation module
Demo-friendly digital twin
Vidyut Prajna prototype • read-only planner sidecar • synthetic demo data
Generates 15-minute telemetry for multiple days.
Signals: EV demand, traffic intensity, temperature, rain, humidity and transformer/base load.
Zone archetypes: residential, commercial, IT, logistics and mixed.
Synthetic outputs are transparent and replaceable with real OCPP + DTR telemetry.
EV demand
Daily demand cycles + charger density + traffic + weather effects.
Traffic and weather
Morning/evening congestion, rain bursts, heat impact and humidity.
Grid load
Non-EV base load and transformer capacity per H3 cell.

## Slide 5
4. Spatial modeling with H3 hexagons
Topology-aware city partition
Vidyut Prajna prototype • read-only planner sidecar • synthetic demo data
Representative Bengaluru zones are expanded into H3 cells.
Each cell stores zone type, coordinates, transformer capacity, charger density and growth score.
Neighbor maps support spatial smoothing and local propagation of risk.
Default demo uses H3 resolution 8; resolution 9 can be enabled for finer ward-scale views.
H3 cells become graph nodes
Edges come from H3 neighbors; values come from demand, traffic, weather and grid-load features.

## Slide 6
5. Forecasting model: simplified STGCN equivalent
Lightweight but topology-aware
Vidyut Prajna prototype • read-only planner sidecar • synthetic demo data
Temporal learner
GRU learns short-term demand dynamics from recent time windows.
Spatial signal
H3-neighbor smoothing injects local topology and adjacent-cell effects.
Forecast output
Predicted EV demand per cell and timestamp, used by optimizer.
Features
EV demand history
Traffic intensity
Temperature, rain and humidity
Grid load and risk score
Cyclical hour/day features
Why not full STGCN in prototype?
Avoids heavy graph ML infrastructure.
Runs locally on laptops.
Preserves the key product flow: predict → optimize → explain.

## Slide 7
6. Constraint-aware optimization
Lagrangian/MCDM-inspired scheduler
Vidyut Prajna prototype • read-only planner sidecar • synthetic demo data
Urgent/priority share is served immediately.
Flexible demand is shifted within deadline windows based on vehicle priority and zone type.
Candidate slots are scored by global load, local transformer utilization and delay penalty.
Residual overloads remain visible as risk; no hardware commands are sent.
Objective intuition
minimize peak + variance + local stress
subject to priority service + deadlines + transformer headroom
Point of minimum regret: balance grid health with user service level.

## Slide 8
7. Plotly Dash dashboard
Planner command center
Vidyut Prajna prototype • read-only planner sidecar • synthetic demo data
H3 heatmap
Predicted demand, unmanaged stress, optimized stress and siting score.
Load curve
Base grid, unmanaged forecast and optimized load across the horizon.
Metrics
Peak reduction, variance reduction, stress events and model accuracy.
Dashboard layout
Map + heatmap
Time slider / playback
City load graph
Top zones table
LLM chat panel

## Slide 9
8. LLM integration: UX layer only
Grounded assistant
Vidyut Prajna prototype • read-only planner sidecar • synthetic demo data
Users can ask: “Which areas will have peak demand tonight?” or “Why is this zone high risk?”
The LLM receives structured JSON context from the current dashboard state.
Prompt rules: do not predict, do not optimize, do not invent numbers or zones.
Without an API key, the app still runs using a deterministic local explanation fallback.
Inputs
Selected time, top zones, stress ratios, traffic/weather, metrics.
Outputs
Human-friendly explanations and planning recommendations.
Guardrail
Forecasting and optimization remain Python modules, not LLM tasks.

## Slide 10
9. Demo results from prototype run
Simulated Bengaluru data
Vidyut Prajna prototype • read-only planner sidecar • synthetic demo data
Peak reduction
Sample run: ~11% reduction in city aggregate peak load.
Variance reduction
Sample run: large reduction in load variance after valley filling.
Stress events
Transformer stress events reduce as flexible load shifts to lower-utilization slots.
The exact values depend on synthetic seed, H3 resolution, number of cells and forecast horizon. The dashboard recomputes metrics at startup.
Unmanaged evening peak
Optimized night valley fill

## Slide 11
10. Infrastructure planning output
Future-proof corridors
Vidyut Prajna prototype • read-only planner sidecar • synthetic demo data
Ranking combines predicted demand, unmanaged stress, traffic/growth and spare capacity.
Cells with high demand and low headroom become immediate planning candidates.
Cells with high demand but good headroom are candidates for charger expansion.
The dashboard surfaces top zones and H3 cells for field validation.
High demand + low headroom
Grid reinforcement priority.
High demand + high headroom
Fast charger siting opportunity.
Moderate demand + growth
Monitor as future-proof corridor.

## Slide 12
11. Roadmap and next steps
Prototype → pilot
Vidyut Prajna prototype • read-only planner sidecar • synthetic demo data
Phase 1: finalize shadow-pricing objective and validate with synthetic stress tests.
Phase 2: ward-level shadow-mode pilot using real charging, weather, traffic and DTR telemetry.
Phase 3: planner command center for BESCOM infrastructure planning and 2027 buildout analysis.
Technical upgrades: full STGCN/DCRNN, feeder hierarchy, tariff constraints, charger availability and user SLA rules.
Concept
Prototype
Pilot